## Slide 1: Telecom Systems Lab TLEN 5460 Wireless LANs
Jose Santos
University of Colorado Boulder
Network Engineering @ Computer SCience
1/22/2020

## Slide 2: Review
STP
  Purpose?
  Root bridge
  Root port
  Designated port
VLANs
  Purpose?
  Sub-interfaces
  Trunks
  InterVLAN routing

## Slide 3: Switching Lab Learning Objectives

## Slide 4: Wireless Applications
Wireless communications are very common in all areas
Several sectors use wireless more extensively than others:
  Education
  Business
  Industry
  Travel
  Public safety
  Health care

## Slide 5: Education
Educational institutions were among the first to adopt wireless technology
  Instructors can create presentations on a laptop and carry them into any classroom where it will connect automatically to the campus network
  Students can easily connect wirelessly to a campus network
WLAN technology translates into cost savings for schools
  Reduces need for wiring and infrastructure
  Fewer computer labs necessary

## Slide 6: Business
The introduction of wireless access in conference rooms provides all employees with a mobile office
Employees no longer have to compete for an available wired connection or carry cables with them
A Cisco study showed that wireless communications increased productivity by 86 minutes per day per user
Small office/home office (SOHO) business can also benefit from wireless data communications

## Slide 7: Industry
Examples of wireless data transmission can be found in the fields of construction, warehouse management, and manufacturing
Construction examples:
  A problem with materials can be relayed to main office so workers can be routed to other sites to prevent idle time
  Construction equipment (bulldozers and earth graders) have wireless devices that turn them into smart machines capable of precise positioning using a global positioning system (GPS)

## Slide 8: Industry
Warehouse Management examples:
  Forklift trucks can be outfitted with wireless equipment and employees can wear portable wireless inventory devices to scan bar codes
  Warehouse management system (WMS) software manages all warehouse activities
    WMS is tied into network so managers have ready access to up-to-the-minute statistics
  Radio frequency identification (RFID) tags emit a wireless data signal containing an ID number
    Works with WMS to track inventory

## Slide 9: Industry
Manufacturing examples:
  RFID tags are often used
  When additional parts are needed on a production line, workers press call buttons to request stock
  Battery-powered tags transmit the request wirelessly
  Inventory can quickly be delivered to eliminate a slow down in the production line

## Slide 10: Travel
Airlines, commuter rail lines and even ferry boats are now offering wireless data access
Airlines use wireless technology for communication with aircraft and even for flight maintenance
Vehicle-to-vehicle (V2V) communications uses both GPS and wireless to create a network that allows cars to communicate with one another
  Can alert drivers of accidents or traffic hazards ahead of them
  Can also be used to control traffic jams

## Slide 11: Public Safety
Public safety departments using WLANs to communicate information with public safety vehicles
  Large volumes of data can be quickly downloaded to vehicles
    e.g., building floor plans, photographs of criminal suspects, and maps

## Slide 12: Health Care
Wireless LAN point-of-care computer systems allow medical staff to access and update patient records immediately
  Document patient’s medication administration immediately
  Extensive use of RFID tags
    Identify healthcare professionals, patients, medications
  System verifies that medication being administered to correct patient in correct dosage
    Eliminates potential errors and documentation inefficiencies

## Slide 13: Health Care
Documentation process takes place at bedside where care delivered
  Improves accuracy
Hospital personnel have real-time access to latest medication and patient status information
Wireless technology also used in other medical areas:
  e.g., video pills

## Slide 14: Wireless Advantages and Disadvantages: Advantages
Mobility: Primary advantage of wireless technology
  Enables individuals to use devices no matter where users roam within range of network
  Increasingly mobile workforce is characteristic of today’s business world
  WLANs give mobile workers freedom while allowing them to access network resources
  “Flatter” organizations: WLANs give team-based workers ability to access network resources needed while collaborating in team environment

## Slide 15: Wireless Advantages and Disadvantages: Advantages
Access: wireless can provide network access to areas where previously none existed
  Hotspot: Locations where wireless data services are available
  Municipal networks: hotspots typically found in downtown areas, parks and recreation areas and other high-traffic areas
  Advantages of municipal networks:
    More attractive to businesses
    Local police, fire, and municipal workers can use them
    Provide high speed Internet access for free or low cost

## Slide 16: Wireless Advantages and Disadvantages: Advantages
Connectivity: Wireless technologies can provide improved service, extend the reach of networks, and provide a less expensive alternative to wired technologies
  Wireless ISP: provides wireless data access directly to the home instead of a cable or DSL provider
  Backhaul connection: an organization’s internal infrastructure connection between two or more remote locations
    Wireless networks can be used eliminating the costs associated with leasing lines or installing fiber optic cables

## Slide 17: Wireless Advantages and Disadvantages: Advantages
Deployment: Installing network cabling in older/historic buildings difficult and costly
  Wireless LAN is ideal solution
  Eliminating need for cabling results in cost savings
    Significant time savings as well
  Allows offices to reorganize easily
  Wireless LAN technology eliminates certain types of cable failures and increases overall network reliability

## Slide 18: Wireless Advantages and Disadvantages: Disadvantages
Security: Wireless signals broadcast in open air
  Security for wireless LANs is prime concern
    Unauthorized users might access network
      Can often pick up signal outside the building
    Attackers might view transmitted data
    Employees could compromise network security
      could install rogue access points
    Attackers could easily crack existing wireless security
      Older wireless products have very weak security features

## Slide 19: Wireless Advantages and Disadvantages: Disadvantages
Radio Signal Interference: Signals from other devices can disrupt wireless transmissions
  e.g., Microwave ovens, elevator motors, photocopying machines, theft protection devices, cordless telephones
  Physical interference
    Outdoor
Range of Coverage: Some wireless signals only have a range of 10 feet while others extend to over 350 feet
Slow Speed: a packet moving through a wireless network is slower than it would be on a wired network

## Slide 20: Types of Wireless Networks
Four broad categories:
  Wireless personal area networks (WPAN)
  Wireless local area networks (WLAN)
  Wireless metropolitan area networks (WMAN)
  Wireless wide area networks (WWAN)

## Slide 21: Wireless Personal Area Network (WPAN)
WPAN: wireless network designed for hand-held and mobile devices
  Slow transmission speeds
  Close proximity to other devices (max distance is generally 33 feet)
Bluetooth – WPAN technology that uses short-range transmissions
  Enables users to connect wirelessly to devices such as notebook/tablet computers, smartphones, and other portable devices

## Slide 22: Wireless Local Area Networks (WLANs)
WLAN: designed to replace or supplement a wired local area network (LAN)
Devices can communicate within 350 feet
Transmission speeds can range up to 600 Mbps (1 Gbps)

## Slide 23: Wireless Metropolitan Area Network (WMAN)
WMAN: designed for devices in a broader area of coverage or at higher speeds
A WMAN coverage area could range from several city blocks to an entire small city
Some WMAN technologies use light impulses to send and receive data

## Slide 24: Wireless Wide Area Network (WWAN)
WWAN: wireless data network that extends beyond the range of a WMAN
  Can encompass multiple states, regions, or countries
  Can even be a world-wide wireless data network
Long Term Evolution (LTE) modem provides wireless access several miles away from the transmission point at speeds up to 30 Mbps

## Slide 25: Wireless Certifications
Certified Wireless Network Professional (CWNP) organization
  Goal: educate professionals in the technology of enterprise WLAN products
  Help professionals manage a wireless LAN
CWNP offers multiple wireless LAN certifications
  Certified Wireless Network Administrator (CWNA)
    Foundation level wireless LAN certification for the CWNP program
CCNA-Wireless

## Slide 26: Going Wireless
Mobility != Flexibility
  Easier at Layer 2 than Layer 3
  Roaming Users should stay on same subnet
  Extend an existing infrastructure

## Slide 27: Radio Propagation Basics
Electro Magnetic Waves
  Sign Wave
  Positive & Negative
Spectrum (Licensed and Unlicensed)
  2.4 and 5 Ghz
Interference
Multi path Propagation
Frequency vs. Line of Sight
RF Attenuation
Channel Selection
Higher Frequencies / Lower Range / Noise / Throughput

## Slide 28: Media Access Control
CSMA/CA
  Collision Avoidance (vs Collision Detection)
  Request to Send (RTS)
  Clear to Send (CTS)
  Back off Algorithm (Random number before Re-TX)
  All Frames must be acknowledged
    (except Multicast and Broadcast from AP)
  Wireless transceivers are usually half duplex

## Slide 29: Wireless Standards Organizations and Regulatory Agencies
Several organizations provide direction, standards, and accountability in wireless technology
  International Telecommunication Union Radio Communication Sector (ITU-R)
  US Federal Communications Commission (FCC)
  International Organization for Standardization (ISO)
  Institute of Electrical and Electronics Engineers (IEEE)
  Wi-Fi Alliance

## Slide 30: Wireless Standards
802.11a
  5GHz Spectrum / OFDM / 54Mbps / 27Mbps throughput
  Less Interference
  Half Range than 802.11b
  Not Popular
  Indoor Range (40ft - 54Mbps, 300ft - 6 Mbps)
  Outdoor (100ft -54Mbps, 1000ft - 1 Mbps)
  8 non overlapping channels supported
802.11b
  2.4GHz / DSSS / 11Mbps / 5 - 6 throughput
  1,2,5.5 and 11Mbps Depending on Signal Strength
  Affordable / Popular / Hackable
  “Sufficient Speed for Average user”
  Indoor Range (100ft - 11Mbps, 300ft - 1 Mbps)
  Outdoor (400ft -11Mbps, 1500ft - 1 Mbps)
  3 non-overlapping Channels Supported (11 available)

## Slide 31: Wireless Standards
802.11g
  2.4GHz / OFDM / 54Mbps / 20-25 Mbps throughput
  Indoor Range (100ft - 54Mbps, 300ft - 1 Mbps)
  Outdoor (400ft -11Mbps, 1500ft - 1 Mbps)
  Backwards Compatible with 802.11b
    Slower Speeds
  Non-overlapping channels – 1, 6, 11
802.11n
  Multiple antennas
    MIMO – Multiple-input multiple-output
  600 Mbps
  5GHz & 2.4GHz
802.11ac
  5GHz Band
  1 Gbps

## Slide 32: Wireless Standards
Bluetooth
  2.4GHz frequency hopper (1600/sec) / 720Kbps Max
  Personal Area Network (PAN)
  Low Powered (1mW) - Minimal Interference to 802.11b
  Replaces other wires
900MHz
  Baby Monitors/Phones/Video Cameras
  Low Frequency Better Coverage (through walls easier)
  Cisco Aironet Bridges / WaveLAN
Data over Cellular
  CDPD (TDMA)
  1xRTT (CDMA)
  GPRS (GSM) EDGE Network
  LTE

## Slide 33: Wireless Equipment
Wireless Adapter (NIC)
  External / Internal
Wireless Access Point (WAP)
  Connection to one network
  Bridge Behavior
  Contain Frame on Wireless or Forward to Wired
  L2 Forwarding / Fast!
  Types
    Point to Point (Ethernet to Wireless adapters)
    Point to Multipoint (Standards AP)
  Virtual Access Point (VAP)
  802.11F (IAPP) To track users between multiples APs
  http://systems.cs.colorado.edu/downloads/802-standards/ieee-802.11f.pdf

## Slide 34: Wireless Equipment
Wireless Router
  Connection to Multiple Networks
  Layer 3 Forwarding for every packet vs. directed traffic
  Network Address Translation
  DHCP
  Port Based Control / Filtering / Firewall
    MAC
    URL
    IPSec Sessions
    VPN Support
  Access Controller (AC)

## Slide 35: Wireless Equipment
Wireless Repeater
  Extend the range of an existing WLAN
  Regenerates a Network Signal
  Does not physically connect by wire to any part of the network
  They reduce throughput on the WLAN
  A repeater must receive and retransmit each frame on the same RF channel, which effectively doubles the number of frames that are sent.
  Configure SSID of Root AP to serve
  If multiple APs, one with better signal (Configurable by MAC also)

## Slide 36: Network Types
Independent (ad-hoc)
  Direct connection between users (hub)
  Temporal Networks (Meetings, file exchange)
Infrastructure
  All traffic goes across AP/Router (two step communication)
  Range to AP not between users
  Users associated with only one AP at the time
  No limit on the number of users an AP may serve / throughput
  Hardware
  Business vs. Home
    Antenna not associated to device
    Multiple wireless interfaces (User density)
    IAPP

## Slide 37: Connecting to an AP
SSID (Service Set Identifier)
  Differentiates one WLAN from another
  VLANs
Frequency used (2.4 or 5)
Power
Channel
Mode (Ad-hoc, Infrastructure)
AP MAC Address
Data Rate
  Distance reduces throughput

## Slide 38: Distribution System
Wired interconnection between APs

## Slide 39: Wireless Deployment
Flexibility vs. Security
Site Survey (Wireless Environment)
  Business Requirements
  Number and types of clients, topology of network, types of media, etc.
  Indoor and Outdoor Requirements
  Infrastructure Connectivity Requirements
  Security
  Signal Strength / Coverage / Throughput
  Cost
  Antenna / AP combinations
  Building Construction Materials
  Identify Sources of Interference (Microwave Ovens, Phones, Other Businesses)

## Slide 40: Wireless Deployment
Security
  Radio Environment (antennas on parking lots)
  SSID (Service Set Identifier)
    Non-broadcast Mode
    Change from default
  Differentiates one WLAN form another
  32-character ID attached to the header of Packets (“Sniffable”)
  WEP - Wireless Equivalent Privacy
    “Crackable”
    Key Renewal Cycle (Dictionary Attack)
    Only Secures the “Wireless Part” (Man in the Middle)
  WPA – Wi-Fi protected Access
    WPA2
  MAC Filtering
    Administration Overhead
    Sniff and Change MAC

## Slide 41: Wireless Deployment
Network Design
  Separate the wireless LAN from the rest of the corporate network through a router or separate virtual LAN (VLAN).
  Users and firewalls: VPNs
  Wireless VLANs (combine SSID and IP addressing- DHCP or Fixed)

## Slide 42: Beyond the Lecture
Security Fixes
  IEEE 802.1X
  802.11i
  WPA—Wi-Fi Protected Access
  EAP
  TKIP
802.11F (IAPP)
  Describes AP communications among multi vendor systems
  AP Registration
  Track Roaming Users
  Helps fast hand-off from AP to AP
Vendor Specific Alternatives

## Slide 43: Beyond the Lecture - Troubleshooting
WLAN configuration settings that may cause problems:
  Cochannel interference
  Adjacent-channel interference
  Power settings
  System throughput
    Distance, number of users, processor of AP, packet size
  Incorrect AP configuration settings
    SSID, Security, IEEE 802.11, NIC
  Device, location, distance from AP

## Slide 44: POE
Power over Ethernet
  Power IP phones or wireless AP’s using the same Ethernet cabling
  Since copper Ethernet can reach 100 meters, POE must do so as well
  15Watts
  803.af & Cisco inline power
  Use same pairs 1,2 3,6 or 4,5 7,8
  Resistor between powered pairs at receiver indicate compatibility, change resistance value to indicate voltage.

## Slide 45: Configuring Access Points
Wireless LAN Controller and Access Point configuration example
  http://www.ciscosystems.com/en/US/products/ps6366/products_configuration_example09186a0080665cdf.shtml
Cisco WLAN Contrller Configuration guide
  http://www.cisco.com/en/US/products/ps6366/products_configuration_guide_book09186a00806b0077.html
VLAN configuration guide for cisco WLC
  http://www.ciscosystems.com/en/US/tech/tk722/tk809/technologies_configuration_example09186a008073c723.shtml