## Slide 1: Telecom Systems Laboratory CYBR 7000 Routing Protocols
Jose Santos
Network Engineering @ Computer Science

## Slide 2: IP Subnetting
Copyright © 2007-19 by Jose Santos

## Slide 3: IP Subnetting
Given a Single Class B subnet /24. Support the following network.

## Slide 4: IP Subnetting
Don’t forget
Subnet Zero
Broadcast Address
Your Router DG IP address
Your Management IP addresses

## Slide 5: IP Subnetting (Homework)
Given a Single Class B subnet /23. Users X 2

## Slide 6: IP Subnetting (Homework)
Given a Single Class B subnet /24. Users X 2. Networks X 2

## Slide 7: Sample Midterm Q
Design Ip addressing needed for this customer:
  4 sites, each with 20 buildings, each with 3 floors, each with 3 different set of users, 109 users of each type per floor. 1 building from each site needs secure network connectivity to other sites, assume you have both public internet access and a private network (assume proper IP addressing: public/private), ensure if one network is down you can still have connectivity between users/sites, ISP is giving you 2 public IP addresses per site.

## Slide 8: Routing Protocols

## Slide 9: Overview and Terminology
Think beyond directly connected devices
“Network Map” and Routing tables
Static Routes (type the Internet)
Routing protocols: Propagate information about available networks
Routed protocols: L3, protocols that can be routed
Routing type: Link state vs. distance vector
Exterior Routing Protocols: Inter-corporate route distribution
Interior Routing Protocols: Intra-corporate route exchange
Autonomous System: Network under single mgmt/control (ISP)

## Slide 10: Routing objectives
Build a routing table (learn & propagate)
Pick best routes (if more than 1 available)
Remove invalid routes
Replace routes if better advertisement received
Restore routes fast (convergence time)
Prevent loops

## Slide 11: Exterior Routing Protocols
Border Gateway Protocol (BGP)
  Used to exchange route information between AS’s
  Cares more about global connectivity rather than specific
  Uses TCP
  Route exchange is performed with well know neighbors
  Every organization has a AS number that uniquely identifies them
  Routes are selected on basis of policy / business relationships not on metrics / network parameters
  AS prepending prevents loops
  Routing tables exceed 1000,000 routes

## Slide 12: BGP Example

## Slide 13: Interior Routing Protocols
  Type of routing protocol
    Distance vector
    Link-state
    Hybrid
  Update process
    Full updates
    Partial updates
  Convergence time
  Metric
    Measure of link quality / preference
  VLSM support
    Subnet size variations
    Permit better address allocation
  Classless vs. Classful
    TX or Not TX mask info
    IF TX then VLSM supported
Several available in the market. Protocols have evolved over time to respond to changing network conditions
Considerations while choosing a protocol:

## Slide 14: Distance Vector Protocols
DV Logic
  Add directly connected
  Send updates out include directly connected and learned routes
  Listen for routing updates
  Routing info: subnet & metric
  Use broadcast or multicast for updates
  Chose best of multiple routes
  Send/expect periodic full updates
  If updates no longer received, remove routes learned from such neighbor
  Assume that the advertising router is the next hop for a route

## Slide 15: Distance Vector Protocols
RIPv1
  Metric: hop count (smaller better?). Infinite metric = 16
  Full updates every 30s (subnet # & metric)
  Convergence 3-5 minutes (depending on size of routing table)
  Classful (no VLSM)
  Broadcasts updates (255.255.255.255)
RIPv2
  Same features as RIPv1
  Adds: VLSM support (updates include subnet #, mask & metric)
  MD5 and plain text authentication
  Includes next hop router IP on updates
  Uses external route tags (redistribution)
  Multicast routing updates (224.0.0.9)

## Slide 16: Distance Vector Protocols
IGRP
  Proprietary
  Metric: bandwidth + delay (default), reliability, load, MTU
  Metric value (1 - 4 billion), smaller better.
  Metrics are cumulative: multi-hop path adds links delays
  Metrics are configurable
  Full updates every 90s
  No VLSM supported
  Infinite metric = 4,294,967,295 (smaller better)

## Slide 17: Link State Protocols
LS logic
  Add directly connected
  Don’t TX routing info until neighbors are discovered
  Routing info: topological information about the network, at the end every router has a complete map of the network.
  Use reliable protocol for route updates
  Calculate Shortest Path First algorithm (Dijkstra) to determine best routes and next hop (also prevents loops)
  Full updates at start and after long periods of time
  Partial updates when a link fails
  Fast convergence

## Slide 18: Link State Protocols
OSPF
  Most popular
  Discover neighbors, then exchange routes
  Reliable Transport Protocol
  Run SPF and store best routes
  More memory required, more processing
  Metric: “cost” based on bandwidth (smaller-better)
  Averages 10s convergence time
  VLSM supported
  Hello messages to confirm neighbor reachability
  Full updates every 30 min
  Partial updates when link fails

## Slide 19: Link State Protocols
Integrated IS-IS
  OSI original
  Can exchange routing information for multiple L3 protocols
  Full flooding every 15 min
  Metric: Configurable value, smaller better

## Slide 20: Hybrid Protocols
EIGRP
  Proprietary
  Uses features from both link-state and distance vector protocols (balanced hybrid protocol: topology + routing tables)
  Diffused Update Algorithm (DUAL): exchange more info than distance vector but less than link-state
  Demands less computation
  Calculated best and “feasible successor routes” (alternatives), permits immediate convergence.
  Discovers neighbors like OSPF
  Metric based on bandwidth and delay (Idem IGRP * 256)
  Does not send periodic full updates

## Slide 21: Loop prevention in DVP
Problems:
  Multiple routes to same network
  Miscommunications on a single link
  Information loops through alternative paths
  Counting to Infinity

## Slide 22: Loop Prevention in DVP
Solutions:
  Pick up the best
  If tie pick the first one or pick both and due load balancing
  Split horizon
    Don’t TX routes the interface I received it
  Route poisoning
    When a route fails, advertise it with an infinite metric
  Split horizon with poisonous reverse
    If a link fails TX routes on all interfaces but with an infinite metric
  Hold-down timer
    If a route fails don’t accept replacements until some time
    RIP (180s), IGRP (280s)
  Triggered updates
    Send immediate updates after a route fails, don’t wait for update timer

## Slide 23: Multiple Equivalent Routes
First learned / Better Metric
Equivalent (routing config mode)
  maximum-paths number
    defaults to 4, ranges from 1-6
RIP
  hop count
  balances traffic across the various routes
IGRP
  “pretty close metric” concept
  variance multiplier
    routes in the range of lowest metric * variance are considered equal
  traffic-share min
    From multiple valid routes on the table take the one with smaller metric (convergence time!)
  balances traffic in proportion to metric values

## Slide 24: Administrative Distance
Applies to similar routes received from different protocols
Prioritizes different routing protocols (which protocol I believe first?)
Lower the number, the better
Examples:
    Directly connected 0
    Static Routes 1
    EIGRP (internal) 90
    IGRP 100
    OSPF 110
    IS-IS 115
    RIP 120
    EIGRP (external) 170

## Slide 25: “show ip route”
Router1#show ip route
  Codes: C - connected, S - static, I - IGRP, R - RIP, M - mobile, B - BGP
  D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
  N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2
  E1 - OSPF external type 1, E2 - OSPF external type 2, E - EGP
  i - IS-IS, L1 - IS-IS level-1, L2 - IS-IS level-2, * - candidate default
  U - per-user static route, o - ODR
  Gateway of last resort is not set
  10.0.0.0/8 is variably subnetted, 6 subnets, 3 masks
  O 10.0.142.0/30 [110/74] via 10.0.144.2, 00:00:46, Ethernet0
  C 10.0.144.0/24 is directly connected, Ethernet0
  O 10.0.148.1/32 [110/75] via 10.0.144.2, 00:00:46, Ethernet0
  171.68.0.0/26 is subnetted, 1 subnets
  C 171.68.178.192 is directly connected, Ethernet0
  172.68.0.0/16 is variably subnetted, 2 subnets, 2 masks
  I 172.68.0.0/16 [100/8976] via 172.68.1.1, 00:00:02, Serial0
  I 172.68.1.0/32 [100/8976] via 172.68.1.1, 00:00:02, Serial0

## Slide 26: RIB vs FIB
R 193.108.0.0/17 [117] via 21.2.2.2, 00:16:17, Ethernet0/0
S 193.108.0.0/17 [117] via 24.2.2.2, 00:16:17, Ethernet0/1.3
OIA 193.108.0.0/16 [110/84] via 2.2.2.2, 00:16:17, Ethernet0/0
R 107.12.10.0/24 [110] via 7.7.7.7, 00:12:15, Ethernet0/4
OE1 107.12.10.0/24 [110] via 7.7.7.7, 00:12:15, Ethernet0/4
D 192.16.10.0/24 via 192.17.100.5, 00:00:16, Serial0/0
O 192.16.10.0/24 [AD: ] via 192.19.100.5, 00:00:16, Serial0/0
C 192.20.2.0/24 is directly connected, Ethernet0/0
R 192.20.2.0/24 [AD: ] via 4.3.3.2, 00:11:19
R 192.16.10.0/24 via 192.16.100.5, 00:00:16, Serial0/0

## Slide 27: Extended Ping
Ping’s IP source address is by default the one of the exit interface
We are in a router. How can we test if a ping would work from one of the client stations?
    Router#ping
    Protocol [ip]:
    Target IP address: 10.10.10.232
    Repeat count [5]:
    Datagram size [100]:
    Timeout in seconds [2]:
    Extended commands [n]: y
    Source address or interface: 10.10.20.1
    Type of service [0]:
    Set DF bit in IP header? [no]:
    Validate reply data? [no]:
    Data pattern [0xABCD]:
    Loose, Strict, Record, Timestamp, Verbose[none]:
    Sweep range of sizes [n]:
    Type escape sequence to abort.
    Sending 5, 100-byte ICMP Echos to 10.10.10.232, timeout is 2 seconds:

## Slide 28: VRF
VLAN Concept for layer 3 devices
Separate control plane
  -Define VRF
  -Port Membership
  -Configuration/show commands include vrf name
  show ip route vrf vrf-name