## Slide 1: Telecom Systems Laboratory TLEN 5460 Advanced Routing Route summarization, VLSM Classless and Classful Routing
Jose Santos
Interdisciplinary Telecommunications Program

## Slide 2: Advanced Routing
Route summarization, VLSM Classless and Classful Routing

## Slide 3: OSPF Routing
Single Area
Multi- Area
  LSA table size
  Limit Updates
Area 0 Connectivity
  Virtual Link
Route Summarization

## Slide 4: Route Summarization
Reduce size of routing tables (less memory)
Faster Routing (less lookup time)
Improve convergence time (specific vs. generic routes)
Troubleshooting
Routing protocols must support VLSM when the network uses route Summarization

## Slide 5: No summarization

## Slide 6: Summarization
Summary routes are configured by network administrators, and configuration differs depending on routing protocol
Subnet choices and contiguous IP addresses are critical
Routers advertise summary routes instead of specifics.

## Slide 7: VLSM
VLSM (Variable-Length Subnet Mask)
  More than one mask is used within a single class network
  Mask bits are allocated to maximize IP utilization
    Serial links
      Point to Point
      /30 255.255.255.252 2^2 -2 = 2 Addresses
    LAN
      Dependent on No of Hosts
  Requirements:
    Subnets must not overlap
    Subnets must be contiguous
    Routing protocol must support VLSM (TX Subnet Number + Mask)
      RIPv2, EIGRP & OSPF

## Slide 8: Determining “Best” Summary Route
Find Common Part
    11.3.1.0 0000 1011 . 0000 0011 . 0000 0001 . 0000 0000
    11.3.2.0 0000 1011 . 0000 0011 . 0000 0010 . 0000 0000
    11.3.3.0 0000 1011 . 0000 0011 . 0000 0011 . 0000 0000
    11.3.4.0 0000 1011 . 0000 0011 . 0000 0100 . 0000 0000
Repeat Common and Fill with 0’s
    11.3.0.0 0000 1011 . 0000 0011 . 0000 0000 . 0000 0000
Create Mask that meets common part
    255.255.248.0 1111 1111 . 1111 1111 . 1111 1000 . 0000 0000
Verify Range
    256-248 = 8 // Networks 0, 8
    first IP 11.3.1.1
    last IP 11.3.7.254
    Broadcast 11.3.7.255

## Slide 9: Determining “Best” Summary Route
Find Common Part
    11.3.10.0 0000 1011 . 0000 0011 . 0000 1010 . 0000 0000
    11.3.11.0 0000 1011 . 0000 0011 . 0000 1011 . 0000 0000
    11.3.12.0 0000 1011 . 0000 0011 . 0000 1100 . 0000 0000
    11.3.13.0 0000 1011 . 0000 0011 . 0000 1101 . 0000 0000
Repeat Common and Fill with 0’s
    11.3.8.0 0000 1011 . 0000 0011 . 0000 1000 . 0000 0000
Create Mask that meets common part
    255.255.248.0 1111 1111 . 1111 1111 . 1111 1000 . 0000 0000
Verify Range
    256-248 = 8 // Networks 0,8,16
    first IP 11.3.8.1
    last IP 11.3.15.254
    Broadcast 11.3.15.255

## Slide 10: Classless and Classful Routing Protocols
Classful
  Abide by rules of Class A,B,C
  Do not TX mask, just network numbers
  SLSM (Static Length Subnet Mask)
  Router assumes a mask on basis of local config &/or autosummarization
  RIP1 & IGRP
Classless
  Not constrained by class rules
  TX mask & network numbers
  VLSM Support
  RIPv2, OSPF & EIGRP

## Slide 11: Classless and Classful Routing Protocols
Autosummarization
  When a router has interfaces in more than one class A,B or C network,
  Routes within “route” updates are summarized when TX to different network.
  RIP and IGRP perform it by default and cannot be disabled
  RIPv2 can be enabled or disabled.
  EIGRP runs it by default but can be disabled as well

## Slide 12: Classless and Classful Routing Protocols
Contiguous and Discontiguous Networks
  Classful routing protocols do not support networks with discontiguous networks
  Center router will have two output interfaces to same network, load balancing is performed

## Slide 13: Classful and classless Routing
Routing
  Process of Forwarding IP packets
Classless/Classful
  Consider or ignore class rules.
  Class concepts are totally independent of the routing protocol.
Classless & Classful routing determine how a router uses a Default route.
  Default route
    If no route found on routing table packet is discarded
    By configuring a Default route, packets are forwarded according to this route (not-discarded)

## Slide 14: Classful and classless Routing
Default Route (Think Router’s default gateway)

## Slide 15: Classful and classless Routing
Default Route
  If you don’t have a specific route to a direction, sent it to such IP
  Static Route Command
      ip route subnet_number subnet_mask next_hop_IP_address
      ip route 0.0.0.0 0.0.0.0 Gateway_IP_address
        0.0.0.0 0.0.0.0 matches all destinations (by convention)
      Propagation by RIP:
        show ip route (gateway of last resort)
  IP default-network Command
      Use it if you have all your subnets in your routing table, and you want to connect to other networks by a default route
      Think partial default
      ip default-network 10.0.0.0 propagated by central router to 11.0.0.0
      show ip route at central displays (* 10.x) as candidate to be default route
      show ip at router “11” displays (* 0.x ) as candidate (RIP specific)

## Slide 16: Classful and classless Routing
Matching Logic
  Classful Routing
    Match Class for destination network
      If the Class Network is found in routing table
        Look for the specific subnet
        If NOT found, discard packet
      If the Class Network is NOT found in routing table
        If Default Route available, use it
        Else discard packet
    Use default route when a destination Class A,B,C network is not in the routing table
  Classless Routing
    Look for a specific route to a destination network
      If found use route
      If NOT found use Default Route

## Slide 17: Classful and classless Routing
Selecting Routing type
  Global Configuration mode
    ip classless (Ignore class rules, use default if not found)
    no ip classless

## Slide 18: Review for next lecture
Redistribution
Administrative Distance
NAT/PAT
Access Lists