## Slide 1: MPLS FUNDAMENTALS
Spring 2019

## Slide 2: North American Long haul Networks
Notes: Reference: North America Long haul networks

## Slide 3: Agenda
Why MPLS?
MPLS Architecture
LDP operation
Traffic Engineering
Convergence
MPLS Applications

## Slide 4: Switching methods on a Router
Process Switching
  Central CPU performs destination IP address lookup for every packet
Fast Switching
  Cache built on demand
  What about a router on the Internet with 400k routes?
CEF
  Pre built switching table
  FIB and Adjacency table(ARP, Inverse ARP)
  Recursively resolves the N.H
Notes: Process switching, fast switching and cef (topology based). With cef being the default these days
Manipulating cost, Unequal cost load balancing..(Requires lot of configuration changes. Lookup based on destination IP address)
Traditional reasons for MPLS: Faster lookups. (Layer 2.5)
Adv of MPLS: TE (source can decide) , Multi protocol transport (Similar to IP), Voice, IP, IPV6, IPX, L2VPN, L3 VPN, BGP free core, Creating VC’s can be tedious, Unified Infrastructure

## Slide 5: Why MPLS?
Bandwidth utilization
Scalable and easy provisioning
Single infrastructure that supports different applications
Can transport multiple protocols other than IPv4
BGP free Core
VPN services (Overlapping IP spaces)
QoS
Control plane vs Forwarding plane separation
MPLS evolution
Notes: Process switching, fast switching and cef (topology based). With cef being the default these days
Manipulating cost, Unequal cost load balancing..(Requires lot of configuration changes. Lookup based on destination IP address)
Traditional reasons for MPLS: Faster lookups. (Layer 2.5)
Adv of MPLS: TE (source can decide) , Multi protocol transport (Similar to IP), Voice, IP, IPV6, IPX, L2VPN, L3 VPN

## Slide 6: Traffic Engineering

## Slide 7: MPLS Overview
MPLS versus Frame Relay
Notes: MPLS – Distribution of labels taken care automatically via LDP.
Protocol ID in MPLS? How will LSR’s know what is the MPLS payload?

## Slide 8: MPLS Overview
MPLS Header
Notes: MPLS – Distribution of labels taken care automatically via LDP.
Protocol ID in MPLS? How will LSR’s know what is the MPLS payload?

## Slide 9: Question?
How does a router identify that it received a labelled packet or an IP packet?
Notes: LSP’s can be assigned statically (not popular) and dynamically using (LDP,RSVP,BGP)
Running a separate protocol for distributing labels.
Ingress determines the FEC

## Slide 10: MPLS Terminologies
RIB, FIB, LIB, LFIB & Adjacency Table
Ingress, Egress, Transit
Upstream, Downstream, Edge LSR, LSR, LSP (Nested LSP), FEC
Local bindings, Remote bindings & Label Operations (Push, Pop, swap)
Protocols to distribute labels( Static LSP, LDP, RSVP,BGP)
Notes: LSP’s can be assigned statically (not popular) and dynamically using (LDP,RSVP,BGP)
Running a separate protocol for distributing labels.
Ingress determines the FEC

## Slide 11: MPLS Terminologies
Notes: LSP’s can be assigned statically (not popular) and dynamically using (LDP,RSVP,BGP)
Running a separate protocol for distributing labels.
Ingress determines the FEC

## Slide 12: MPLS Architecture
Notes: LSP’s can be assigned statically (not popular) and dynamically using (LDP,RSVP,BGP)
How does a router know whether it’s a IP packet or a labelled packet? Label lookup vs cef lookup

## Slide 13: MPLS Architecture
Control plane and Data plane

## Slide 14: MPLS Architecture

## Slide 15: MPLS Architecture

## Slide 16: Different MPLS Modes
MPLS Label Spaces ( Per-platform & Per-Interface)
Label Distribution modes (DoD, UD)
Label Retention modes (LLR, CLR)
LSP control modes (Independent & Ordered)

## Slide 17: Overview of LDP
Labels assigned by downstream peer
Limitations
    LSPs follow the conventional IGP path
    Does not support explicit routing
Upstream
LDP peer
Downstream
LDP peer
LSR
3
2
5
4
1
3
Net: 10.0.0.0
Label: 52
(3, 29)
Net: 10.0.0.0
Label: 29
MPLS Table
In
Out
(2, 52)
MPLS Table
In
Out
(1, 17)
MPLS Table
In
Out
(5, 52)
Receive
outgoing
label
(4, 17)
Net: 10.0.0.0
Label: 17
Advertise
incoming
label
(3, 35)

## Slide 18: Overview of LDP
Reserved Labels
PHP improves performance in the egress LSR’s( Label stack)
Notes: Label 0-> Explicit null (EXP bits removed if the label is removed. QOS to be delivered to egress LSR. Label value of 0. Copying QOS to precedence bits in IP )
Label 1->Router Alert label ( Alerts that the packet needs a closer look. Software process.
Label 3-> Implicit Null (Default , egress LSR assigns label 3 to its connected and summarized prefixes, Avoid double lookups, PHP)
Label 14->OAM Alert table
Unreserved range in cisco : 16 – 100,000

## Slide 19: Overview of LDP
Discovery of LSR’s running LDP
Session Establishment and maintenance
Advertisement of label mappings
Notifications

## Slide 20: Overview of LDP
Hello messages

## Slide 21: LDP Neighbor Discovery

## Slide 22: LDP Neighbor Discovery

## Slide 23: LDP Neighbor Discovery

## Slide 24: LDP Neighbor Discovery
An LDP session is established from the router with the higher IP address.

## Slide 25: LDP Session Negotiation
Peers first exchange initialization messages.
The session is ready to exchange label mappings after receiving the first keepalive.

## Slide 26: LDP Session Negotiation

## Slide 27: Label Allocation - Building IP Routing Table
  IP routing protocols are used to build IP routing tables on all LSRs.
  FIBs are built based on IP routing tables with no labeling information.

## Slide 28: Label Allocation - Allocating Labels
  Every LSR allocates a label for every destination in the IP routing table.
  Labels have local significance.
  Label allocations are asynchronous.

## Slide 29: Label Allocation - LIB and LFIB Setup
  LIB and LFIB structures have to be initialized on the LSR allocating the label.

## Slide 30: Label Distribution and Advertisement
The allocated label is advertised to all neighbor LSRs, regardless of whether the neighbors are upstream or downstream LSRs for the destination.

## Slide 31: Label Distribution and Advertisement (Cont.)
Every LSR stores the received label in its LIB.
Edge LSRs that receive the label from their next hop also store the label information in the FIB.

## Slide 32: Label Distribution and Advertisement (Cont.)
Forwarded IP packets are labeled only on the path segments where the labels have already been assigned.

## Slide 33: Label Distribution and Advertisement (Cont.)
Forwarded IP packets are labeled only on the path segments where the labels have already been assigned.

## Slide 34: Label Distribution and Advertisement (Cont.)
  Forwarded IP packets are labeled only on the path segments where the labels have already been assigned.

## Slide 35: Label Distribution and Advertisement (Cont.)
Every LSR will eventually assign a label for every destination.

## Slide 36: Label Distribution and Advertisement (Cont.) Receiving Label Advertisement
  Every LSR stores received information in its LIB.
  LSRs that receive their label from their next hop LSR will also populate the IP forwarding table (FIB).

## Slide 37: Label Distribution and Advertisement (Cont.) Receiving Label Advertisement
  Every LSR stores received information in its LIB.
  LSRs that receive their label from their next hop LSR will also populate the IP forwarding table (FIB).

## Slide 38: Populating LFIB
  Router B has already assigned a label to network X and created an entry in the LFIB.
  The outgoing label is inserted in the LFIB after the label is received from the next hop LSR.

## Slide 39: Packet Propagation Across an MPLS Network

## Slide 40: Packet Propagation Across an MPLS Network

## Slide 41: Packet Propagation Across an MPLS Network

## Slide 42: Packet Propagation Across an MPLS Network

## Slide 43: Normal TTL Operation
Cisco routers have TTL propagation enabled by default.
On ingress: TTL is copied from IP header to label header.
On egress: TTL is copied from label header to IP header.

## Slide 44: Normal TTL Operation

## Slide 45: Normal TTL Operation

## Slide 46: TTL and Loop Detection
  Labeled packets are dropped when the TTL is decreased to 0.

## Slide 47: Disabling TTL Propagation
  TTL propagation can be disabled.
  The IP TTL value is not copied into the TTL field of the label, and the label TTL is not copied back into the IP TTL.
  Instead, the value 255 is assigned to the label header TTL field on the ingress LSR.
  Disabling TTL propagation hides core routers in the MPLS domain.
  Traceroute across an MPLS domain does not show any core routers.

## Slide 48: Traceroute with Disabled TTL Propagation
  The first traceroute packet (ICMP) that reaches the network is dropped on router A.
  An ICMP time-to-live exceeded message is sent to the source from router A.

## Slide 49: Traceroute with Disabled TTL Propagation (Cont.)

## Slide 50: Traceroute with Disabled TTL Propagation (Cont.)
The second traceroute packet that reaches the network is dropped on router D.
An ICMP time-to-live exceeded message is sent to the source from router D.

## Slide 51: Impact of Disabling TTL Propagation
  Traceroute across an MPLS domain does not show core routers.
  TTL propagation has to be disabled on all label switch routers.
  Mixed configurations (some LSRs with TTL propagation enabled and some with TTL propagation disabled) could result in faulty traceroute output.
  TTL propagation can be enabled for forwarded traffic only—traceroute from LSRs does not use the initial TTL value of 255.

## Slide 52: Command Reference
  mpls ip
  Show mpls interface
  Show mpls ldp discovery
  Show mpls ldp bindings
  Show mpls forwarding-table

## Slide 53: AGENDA
Why MPLS?
MPLS Architecture
LDP operation
Traffic Engineering
Convergence
MPLS Applications

## Slide 54: Traffic Engineering

## Slide 55: Motivations for Traffic Engineering
What is the Path chosen by LDP LSP?
Source-based routing
Takes in to account Bandwidth available on link, delay, attributes
Increase efficiency of bandwidth resources
Override the shortest path chosen by IGP
$$$$ Saving

## Slide 56: Traffic Engineering
Popular protocols used for TE
Constrained-Based Shortest path
  Bandwidth, Affinity/Link Attributes, Priority
TE tunnels are _________ directional?

## Slide 57: THE TE SOLUTION
R8
R2
R6
R3
R4
R7
R5
R1
MPLS Labels can be used to engineer explicit paths
Normal path: R8  R2  R3  R4  R5
Tunnel path: R1  R2  R6  R7  R4
30Mbps traffic to R5
20Mbps traffic to R5
30Mbps traffic to R5 from R8
20Mbps traffic to R5 from R1

## Slide 58: Traffic Engineering
LSP calculated at the head end
Which Routing protocol to use?

## Slide 59: Traffic Engineering Components
Information Distribution
Path selection and calculation or CSPF
Path setup (RSVP)
Trunk Admission Control
Path maintenance
Forwarding traffic on to a TE tunnel
Notes: IGP to flood TE extensions! OSPF opaque area (LSA 10) and IS-IS uses TLV’s

## Slide 60: Path Setup Example
R8
R2
R6
R3
R4
R7
R1
R5
R9
49
32
Pop
22
27
RSVP PATH: R1  R2  R6  R7  R4  R9
RSVP RESV: Returns labels and reserves bandwidth on each link Bandwidth available
Returned label via RESV message
PATH message
20Mbps
RESV message
80
60
100
70
30
49
80
60
40
80
50
10

## Slide 61: RSVP Operation Overview

## Slide 62: Extended RSVP
RSVP message types
  PATH: Establish state and request label assignment
  RESV: Distribute labels & reserve resources
Runs ingress-to-egress, not end-to-end
RESV
PATH
R1
R4
R8
R9
Ingress
LSR
Egress
LSR
Explicit route = {R1, R4, R8, R9}

## Slide 63: Path Message Extensions
Transmitted by ingress LSR towards the egress LSR to establish an LSP tunnel
Addressed to the egress LSR and contains a router alert option in its IP header indicating that the datagram requires special processing by intermediate routers
Includes a number of different RSVP objects
  Label Request Object (M)
  Session Object (M)
  Explicit Route Object-ERO (O)
  Record Route object-RRO (O)
  Session Attribute Object (O)

## Slide 64: Extended RSVP – PATH Message
Explicit route is passed to R1
R1 transmits a PATH message addressed to R9
  Label Request Object
  ERO = {strict R4, strict R8, strict R9}
  Session object identifies LSP name
  Session Attributes: Priority, preemption, and fast reroute
  Sender T_Spec: Request bandwidth reservation
Establish Path
State Block
Establish Path
State Block
Establish Path
State Block
Ingress
LSR
Egress
LSR
Explicit route = {R1, R4, R8, R9}
PATH
ERO= {R4, R8, R9}
PATH
ERO= {R8, R9}
PATH
ERO= {R9}
R1
R4
R8
R9

## Slide 65: Resv Message Extensions
Transmitted from egress LSR toward the ingress LSR in response to the path message
Establishes path state in each LSR by distributing label bindings, requesting resource reservations along the path, and specifying the reservation style
Includes a number of different RSVP objects
  Label Object (M)
  Session Object (M)
  Style Object (M)
  Record Route object-RRO (O)

## Slide 66: Extended RSVP – RESV Message
R9 transmits a RESV message to R8
  Label = 3 (indicates that penultimate LSR should Pop header)
  Session object to uniquely identify the LSP
R8 and R4
  Stores “outbound” label, allocate an “inbound” label
  Transmits RESV with inbound label to upstream LSR
R1 binds label to FEC
Ingress
LSR
Egress
LSR
R1
R4
R8
R9
RESV
Label = 20
RESV
Label = 3
RESV
Label = 17
MPLS Table
In
Out
(6, 20)
(3, 17)
MPLS Table
In
Out
(2, 17)
IP Route
MPLS Table
In
Out
(5, Pop)
(2, 20)
3
6
2
5
4
2
Penultimate
LSR

## Slide 67: Other Message Extensions
PathTear Messages
  Remove path states as well as dependent reservation states along a path
  Initiated by a sender application or by a router when its path state times out
  Follow the same path as path messages
ResvTear Messages
  Remove reservation states along a path
  Initiated by a receiver application or by a router when its reservation state times out
  Follow the same path as reservation messages

## Slide 68: Other Message Extensions
PathErr Messages
  In case of path errors, due to parameter problems in a path message, the router sends a unicast PathErr message to the sender that issued the Path message
ResvErr Messages
  When a reservation request fails, a ResvErr message is delivered to all the receivers involved

## Slide 69: PathTear & ResvTear Message Flow
PathTear
ResvTear
R1
R4
R8
R9
Ingress
LSR
Egress
LSR
Established LSP
R1
R4
R8
R9
Ingress
LSR
Egress
LSR
Path
PathErr
Resv
ResvErr

## Slide 70: Agenda
Why MPLS?
MPLS Architecture
LDP operation
Traffic Engineering
Convergence
MPLS Applications

## Slide 71: Steady State Description
After the LSRs have exchanged the labels, LIB, LFIB, and FIB data structures are completely populated.

## Slide 72: Link Failure Actions
Routing protocol neighbors and LDP neighbors are lost after a link failure.
Entries are removed from various data structures.

## Slide 73: Routing Protocol Convergence
Routing protocols rebuild the IP routing table and the IP forwarding table.

## Slide 74: MPLS Convergence
The LFIB and labeling information in the FIB are rebuilt immediately after the routing protocol convergence, based on labels stored in the LIB.

## Slide 75: MPLS Convergence After a Link Failure
MPLS convergence in frame-mode MPLS does not affect the overall convergence time.
MPLS convergence occurs immediately after the routing protocol convergence, based on labels already stored in the LIB.

## Slide 76: Link Recovery Actions
Routing protocol neighbors are discovered after link recovery.

## Slide 77: Link Recovery Actions & IP Routing Convergence
IP routing protocols rebuild the IP routing table.

## Slide 78: Link Recovery Actions & IP Routing Convergence
IP routing protocols rebuild the IP routing table.
The FIB and the LFIB are also rebuilt, but the label information might be lacking.

## Slide 79: Link Recovery Actions & MPLS Convergence
  Routing protocol convergence optimizes the forwarding path after a link recovery.
  The LIB might not contain the label from the new next hop by the time the IGP convergence is complete.
  End-to-end MPLS connectivity might be intermittently broken after link recovery.
  Use MPLS Traffic Engineering for make-before-break recovery.
  FRR, Link Protection, Node protection

## Slide 80: MPLS Applications
MPLS VPN
  Layer 2 VPN (AToM, VPLS)
  Layer 3 VPN (VRF, Non-unique IP space)
BGP free core
QoS Guarantee
Notes: Extending Metro Ethernet ( EOMPLS)
Layer 3 VPN

## Slide 81
MPLS Applications

## Slide 82
MPLS Applications

## Slide 83
MPLS Applications

## Slide 84
MPLS Applications

## Slide 85
References
  MPLS Fundamentals, Luc De Ghein
  Juniper MPLS Guide
  Cisco MPLS Guide